## Slide 1: No One is Safe
4 People Getting A’s
David Kim, Alex Dunmire, Rohan Nagarkar, Michelle Dean

## Slide 2: Table of Contents
Goals
Functionality
Successes
Failures
Summary & Tradeoffs

## Slide 3: Goal of the project
To make FPGA controlled cars that can communicate with an Android app controller through wifi or bluetooth…
...And also play laser tag!

## Slide 4
Short Functionality

## Slide 5: Project Attribution
RC Car: Rohan, Alex
power/speed power/rotation FPGA control
Android/FPGA comm.
Car controls
Camera
Laser controls
Android App: David, Michelle
Bluetooth

## Slide 6: Short specification
Crawler
Nexys 3: steer car and control throttle, would capture camera data, send and receive data over wifi
VModCam: film from car’s perspective and output in RGB
Android device: run app, send commands over wifi, receive game data over wifi

## Slide 7: Emulating RC controller w/ FPGA
Measure Emulate

## Slide 8: Emulating RC controller w/ FPGA cont.
100MHz/1953*512 =
10ms
ClkCount = 2^12
20ms period

## Slide 9: LASER Block Diagram
FPGA
Detector
Laser Diode

## Slide 10: LASER BEAMS
Laser Diodes:
  650nm wavelength, 5mW output power
  Operates within 2.7 - 5.2 VDC range
Fires upon Button Press
Connected to PMOD output

## Slide 11: LASER BEAMS CONT.
module laser(clk,pb,laser);
input clk,pb;
output reg laser;
always @(posedge clk)begin
case (pb)
1: laser = pb;
default laser = 0;
endcase
end
endmodule

## Slide 12: LASER DETECTOR
Laser Detector
  Vin: 3.3 VDC
  Vout:
    V hit = 3.3 VDC
    V miss = 50 mVDC

## Slide 13: Android Controller
Controller steering uses Android’s
Accelerometer sensors. Due to limited availability
of gyroscopes on devices, our controller utilizes
control and stabilizes sensitivity using a
high-pass k-filter.
The starting net XYZ coordinate is “zeroed” by
the user which will then be incremented/decremented
by the filtered XYZ values.
After trial and error, the optimal k-value used to reduce noise and consistent control is 0.65f. The cutoff net value is set at +/- 5.0f (90 degrees).

## Slide 14: Android Controller
Filter algorithm:
The data that is transmitted from device to vehicle requires a minimum transmission rate of 1kbps, using 5-bit sequence in 20ms intervals. The syntax of an instruction is as follows.
bits[1:0] Steering Control 00 (no signal) 01 (right) 10 (left)
bits[3:2] 00 (no throttle) 01 (forward) 10 (backwards)
bit[4] 0 (no fire) 1(fire)

## Slide 15: VGA camera
OmniVision 7670
  SCCB Proprietary protocol
  Cheap camera
Tradeoff: VModCam
  Much more expensive
  Simple I2C protocol
  Example code exists online
  Needs Atlys board (expensive battery, lack of PMod)

## Slide 16: Camera block diagram
Obstacles

## Slide 17: Design Tradeoffs
Car
Hack existing Laser Tag toy?
  Nah, making our own is way cooler, (and cheaper)
  Actual Lasers > IR beam of light
Bluetooth vs Wifi?
  B
Cameras?
  Add camera, lose PMod: not a viable option

## Slide 18: Wi-fi
Early complications in trying to utilize a Wi-fi Pmod to transmit control signal to vehicle.
  Much, if not all, of the internet protocol IP cores that are available for fpga’s are implemented using Vivado and C Language.
  The Pmod Wifi module we are using provides a C language library that can be used. However, to incorporate this library into our design requires us to incorporate a tcp/ip protocol stack to our board.
  After much searching, we were able to use Xilinx ISE’s Embedded Development Kit (EDK) and the BSB file provided on Nexys3’s documentation website.
    However, Licensing issues arose (failure to mention incompatible support for ISE 14.7 version)
    Have been able to make some progress recently using older version.
    Might not have enough time to incorporate it in time.

## Slide 19: Bluetooth
Bluetooth
Servos and Speed Controller
UART/USB port
FPGA

## Slide 20: Successes
Servos: Turn Right and Left
Motor Controller: Forward and Reverse Throttle
Shoot Laser Beams!!!

## Slide 21: Fails
OmniVision Camera
  proprietary configuration bus protocol: OV does not provide good documentation on 2 wire SCCB
VModCam
  Requires memory on Atlys board, not enough PMod ports on Atlys for all project components

## Slide 22: Thank you!
Gif from: http://www.animateur-dj-71.com/eclairage.php